## Slide 1: Diagnosing Performance Overheads in the Xen Virtual Machine Environment
Aravind Menon Willy Zwaenepoel
EPFL, Lausanne
Jose Renato Santos
Yoshio Turner
G. (John) Janakiraman
HP Labs, Palo Alto

## Slide 2: Virtual Machine Monitors (VMM)
Increasing adoption for server applications
  Server consolidation, co-located hosting
Virtualization can affect application performance in unexpected ways

## Slide 3: Web server performance in Xen
25-66% lower peak throughput than Linux depending on Xen configuration
Need VM-aware profiling to diagnose causes of performance degradation

## Slide 4: Contributions
Xenoprof – framework for VM-aware profiling in Xen
Understanding network virtualization overheads in Xen
Debugging performance anomaly using Xenoprof

## Slide 5: Outline
Motivation
Xenoprof
Network virtualization overheads in Xen
Debugging using Xenoprof
Conclusions

## Slide 6: Xenoprof – profiling for VMs
Profile applications running in VM environments
  Contribution of different domains (VMs) and the VMM (Xen) routines to execution cost
  Profile various hardware events
Example output
Function name %Instructions Module
----------------------------------------------------------------------
mmu_update 13 Xen (VMM)
br_handle_frame 8 driver domain (Dom 0)
tcp_v4_rcv 5 guest domain (Dom 1)

## Slide 7: Xenoprof – architecture (brief)
Extend existing profilers (OProfile) to use Xenoprof
Xenoprof collects samples and coordinates profilers running in multiple domains
Domain 0
OProfile (extended)
Xenoprof
Domain 1
OProfile (extended)
Domain 2
OProfile (extended)
Domains (VMs)
Xen VMM
H/W performance counters

## Slide 8: Outline
Motivation
Xenoprof
Network virtualization overheads in Xen
Debugging using Xenoprof
Conclusions

## Slide 9: Xen network I/O architecture
Privileged driver domain controls physical NIC
Each unprivileged guest domain uses virtual NIC connected to driver domain via Xen I/O Channel
  Control: I/O descriptor ring (shared memory)
  Data Transfer: Page remapping (no copying)
I/O Driver Domain
Guest Domain
I/O Channel
NIC
Bridge
vif1
vif2

## Slide 10: Evaluated configurations
Linux: no Xen
Xen Driver: run application in privileged driver domain
Xen Guest: run application in unprivileged guest domain interfaced to driver domain via I/O channel
I/O Driver Domain
Guest Domain
I/O Channel
NIC
Bridge
vif1
vif2

## Slide 11: Networking micro-benchmark
One streaming TCP connection per NIC (up to 4)
Driver receive throughput 75% of Linux throughput
Guest throughput 1/3rd to 1/5th of Linux throughput

## Slide 12: Receive – Xen Driver overhead
Profiling shows slower instruction execution with Xen Driver than w/Linux (both use 100% CPU)
  Data TLB miss count 13 times higher
  Instruction TLB miss count 17 times higher
Xen: 11% more instructions per byte transferred (Xen virtual interrupts, driver hypercall)

## Slide 13: Receive – Xen Guest overhead
Xen Guest configuration executes two times as many instructions as Xen Driver configuration
  Driver domain (38%): overhead of bridging
  Xen (27%): overhead of page remapping
I/O Driver Domain
Guest Domain
I/O Channel
NIC
Bridge
vif1
vif2

## Slide 14: Transmit – Xen Guest overhead
Xen Guest: executes 6 times as many instructions as Xen driver configuration
  Factor of 2 as in Receive case
  Guest instructions increase 2.7 times
Virtual NIC (vif2) in guest does not support TCP offload capabilities of NIC

## Slide 15: Suggestions for improving Xen
Enable virtual NICs to utilize offload capabilities of physical NIC
Efficient support for packet demultiplexing in driver domain

## Slide 16: Outline
Motivation
Xenoprof
Network virtualization overheads in Xen
Debugging using Xenoprof
Conclusions

## Slide 17: Anomalous network behavior in Xen
TCP receive throughput in Xen changes with application buffer size (slow Pentium III)

## Slide 18: Debugging using Xenoprof
40% kernel execution overhead incurred in socket buffer de-fragmenting routines

## Slide 19: De-fragmenting socket buffers
Linux: insignificant fragmentation with streaming workload
Socket receive queue
De-fragment
Socket buffer (4 KB)
Data packet (MTU)
Xenolinux (Linux on Xen)
  Received packets: 1500 bytes (MTU) out of 4 KB socket buffer
  Page-sized socket buffers support remapping over I/O channel

## Slide 20: Conclusions
Xenoprof useful for identifying major overheads in Xen
Xenoprof to be included in official Xen and OProfile releases
Where to get it: http://xenoprof.sourceforge.net